## Slide 1
EE136IU • CAPSTONE MINI-PROJECT DEFENSE
TOPIC 04: Data Augmentation &
Noise Resilience for Low-SNR
Target: −10 to +2 dB Evaluation: −10 to +18 dB
EE136: Machine Learning for Wireless Communications | Capstone Mini-Project Brief
Slide 1 of 14
Speaking roles
Member 1: signal model and data Member 2: augmentation and CNN
Member 3: evaluation and live demo
Notes: Replace generic member labels with the team’s actual names before defense. Suggested role allocation only.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 2
TABLE OF CONTENTS
Agenda
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 2 of 14
01
Signal model and data
Slides 3–4
02
Augmentation and network
Slides 5–6
03
Training and benchmarks
Slides 7–10
04
Live demo and discussion
Slides 11–12
Notes: Presentation: 15 minutes. Live demo: 10 minutes. Q&A: 5 minutes. Appendix contains +4 and +14 dB confusion matrices.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 3
01 • VẤN ĐỀ
Low-SNR signal model
Target region: −10 to +2 dB Benchmark grid: −10 to +18 dB
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 3 of 14
Received burst
r[n] = h s[n] + w[n]
w[n]: complex Gaussian noise
SNR = signal power / noise power
r′[n] = r[n] exp(jθ)
At −10 dB
Noise power = 10 × signal power
Baseline accuracy: 22.05%
Chance level for 8 classes: 12.5%
Constant phase offset: θ is fixed across a burst. CFO adds a phase ramp over time.
Notes: Constant phase rotation and CFO are distinct. CFO: r′[n]=r[n] exp(j(2π Δf n/fs+θ0)). Phase overfitting and learned radial features remain hypotheses, not demonstrated mechanisms.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 4
02 • GIẢI PHÁP & KHÁI NIỆM
Dataset and evaluation protocol
Burst-level split, RMS normalization and evaluation provenance
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 4 of 14
Training data
18,000 synthetic bursts
70% train / 15% validation / 15% test
8 classes, 15 SNR levels
[N, 2, 128] float32
Per-burst RMS normalization
PSK, QAM, PAM and FSK families
Evaluation provenance
evaluate.py regenerates 12,000 bursts
Same generation seed: 42
Reported evaluation subset: 1,800
Train/evaluation isolation
requires a dedicated audit
Notes: train.py: 150 samples/class/SNR. evaluate.py: 100 samples/class/SNR. Both generation and split use seed 42. Do not claim independent holdout or zero leakage before comparing burst hashes and generation lineage. Augmentation applies only to training samples. RMS = sqrt(mean(I²+Q²)).
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 5
02 • GIẢI PHÁP & KHÁI NIỆM
RF augmentation during training
Actual probabilities configured in train.py
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 5 of 14
Phase rotation
p = 0.50
θ uniform in [0, 2π)
Gaussian noise
p = 0.40
σ uniform in [0.01, 0.08]
Circular time shift
p = 0.40
k integer in [−8, +8]
Amplitude scaling
p = 0.30
α uniform in [0.85, 1.15]
Sequential transforms on each training sample. Validation and evaluation use no augmentation.
Notes: Values from train.py, overriding RFAugmentationPipeline defaults. The injected noise changes effective SNR. No per-sample calibrated target SNR is enforced by this transform. Phase rotation uses a constant angle for the burst.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 6
03 • IMPLEMENTATION
1D CNN architecture
Same network for baseline and augmented training
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 6 of 14
Input
[N, 2, 128]
Conv block 1
[N, 64, 64]
Conv block 2
[N, 128, 32]
Conv block 3
[N, 256, 1]
Conv1D k=7 / 5 / 3, BatchNorm and ReLU in each block
MaxPool(2) in blocks 1–2 AdaptiveAvgPool1d(1) in block 3
Classifier
Flatten Linear 256→128 ReLU Dropout 0.3 Linear 128→8
Notes: models/network.py. Trainable parameter count in original deck is 175,432; architecture dimensions and operations are shown directly from code. Pooling in block 3 is adaptive averaging, not fixed AvgPool.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 7
03 • IMPLEMENTATION
Training setup and validation
25 epochs, batch size 64, Adam learning rate 0.001
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 7 of 14
Shared training settings
Cross-entropy loss
Adam, lr = 0.001
CosineAnnealingLR
Best validation accuracy checkpoint
Reported validation result
Baseline accuracy 65.33%
Augmented accuracy 66.07%
Loss: 0.8757 vs 0.7670
Loss curves: epoch history is absent from the repository.
Train losses use different input distributions. Their gaps alone do not establish less overfitting.
Notes: Validation figures are those reported in the source deck/README. No complete epoch history is saved by main(). Do not fabricate convergence curves. Models share hyperparameters but a matched-initialization, multi-seed comparison has not been established.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 8
04 • KẾT QUẢ & DEMO
Accuracy across the SNR grid
Selected gains coexist with losses at other SNR levels
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 8 of 14
Chart: SNR (dB)
| -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18
Baseline | 0.22047 | 0.25862 | 0.41748 | 0.54032 | 0.57851 | 0.68254 | 0.73737 | 0.76119 | 0.84615 | 0.80328 | 0.89344 | 0.81818 | 0.82645 | 0.87805 | 0.86726
Augmented | 0.23622 | 0.30172 | 0.41748 | 0.51613 | 0.61157 | 0.65079 | 0.69697 | 0.76119 | 0.81197 | 0.82787 | 0.85246 | 0.81061 | 0.79339 | 0.84553 | 0.84071
At −8 dB
+4.31 pp
At 0 dB
−3.17 pp
Global accuracy: 67.72% baseline / 66.72% augmented
Notes: pp means percentage points. Benchmark is a single reported run and its evaluation provenance requires auditing. Augmentation improves some low-SNR points, ties at −6 dB and loses at −4 and 0 dB. Full source data are embedded in the editable chart.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 9
04 RESULTS
Macro-F1 across the SNR grid
Class-balanced performance complements accuracy
EE136: Machine Learning for Wireless Communications
Slide 9 of 14
Chart: SNR (dB)
| -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18
Baseline | 0.20802 | 0.25283 | 0.37813 | 0.50621 | 0.52283 | 0.68992 | 0.70352 | 0.73924 | 0.80593 | 0.80681 | 0.88131 | 0.81606 | 0.83121 | 0.84621 | 0.85208
Augmented | 0.21125 | 0.29091 | 0.34726 | 0.4906 | 0.55533 | 0.63369 | 0.67876 | 0.76193 | 0.7804 | 0.84116 | 0.83922 | 0.82193 | 0.80053 | 0.83442 | 0.84532
Global Macro-F1: baseline 0.6668 / augmented 0.6614
Notes: Macro-F1 gives equal weight to each class. Source benchmark_results.json. Per-SNR metrics can fluctuate because each SNR has a relatively small evaluation subset.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 10
04 • KẾT QUẢ & DEMO
Class confusion at −4 dB
Row-normalized confusion matrices, values in percent
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 10 of 14
Baseline
 | BP | QP | 8P | 16Q | 64Q | P4 | CF | GF
BPSK | 87 | 0 | 0 | 0 | 0 | 12 | 0 | 0
QPSK | 0 | 35 | 18 | 41 | 0 | 0 | 0 | 6
8PSK | 0 | 13 | 60 | 13 | 13 | 0 | 0 | 0
16QAM | 9 | 0 | 45 | 18 | 18 | 0 | 0 | 9
64QAM | 0 | 10 | 20 | 50 | 20 | 0 | 0 | 0
PAM4 | 25 | 0 | 0 | 5 | 0 | 70 | 0 | 0
CPFSK | 0 | 11 | 6 | 0 | 0 | 0 | 67 | 17
GFSK | 12 | 6 | 0 | 6 | 0 | 0 | 29 | 47
Augmented
 | BP | QP | 8P | 16Q | 64Q | P4 | CF | GF
BPSK | 75 | 0 | 0 | 0 | 0 | 25 | 0 | 0
QPSK | 0 | 18 | 41 | 41 | 0 | 0 | 0 | 0
8PSK | 7 | 13 | 47 | 27 | 0 | 7 | 0 | 0
16QAM | 0 | 9 | 55 | 18 | 9 | 0 | 9 | 0
64QAM | 0 | 0 | 20 | 40 | 30 | 0 | 0 | 10
PAM4 | 25 | 0 | 0 | 0 | 0 | 75 | 0 | 0
CPFSK | 6 | 6 | 6 | 0 | 0 | 0 | 72 | 11
GFSK | 0 | 12 | 0 | 6 | 0 | 0 | 29 | 53
Rows = true class Columns = predicted class Each row totals approximately 100%
QAM and FSK confusions remain. Noise-related overlap is a physical explanation to test.
Notes: Matrices from benchmark_results.json at −4 dB. Values rounded to whole percentages for readability. Off-diagonal errors are observed evidence. Noise overlap is a plausible explanation, whereas feature learning and CFO robustness have not been established.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 11
04 • KẾT QUẢ & DEMO
Interactive demo
Live manipulation of modulation, SNR and phase offset
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 11 of 14
Live sequence
1 Select modulation and SNR
2 Generate a fresh burst
3 Compare both predictions
4 Sweep phase offset and SNR
Backup video status
No recorded MP4 is available
in the repository.
Required before defense:
embed a 30–60 second screen recording
python -m streamlit run app.py
Notes: The official requirement is an embedded 30–60 second MP4 screen recording of the working demo. No such recording is supplied, so this deck cannot meet that requirement yet. Demonstrate both successful and failed predictions without cherry-picking a guaranteed winning example.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 12
05 • Q&A
Findings and remaining checks
Current benchmark supports a limited, mixed result
EE136: Machine Learning for Wireless Communications | Topic 4 Capstone Defense
Slide 12 of 14
Observed result
Some low-SNR gains
Global accuracy decreases 1.00 pp
Global Macro-F1: 0.6668 vs 0.6614
Sensitivity at 80% accuracy
Baseline: 4.91 dB
Augmented: 5.53 dB
Gain G80: -0.62 dB
G80 = SNR80,baseline − SNR80,augmented
First upward crossing, linear interpolation. Single-run estimate with non-monotonic curves.
Next: audit burst isolation, repeat seeds, ablate transforms and test CFO separately.
Notes: First upward 80% crossing calculated from benchmark JSON. Baseline 4.913513513513515, augmented 5.528643216080404, gain -0.6151297025668887 dB. The negative gain means augmentation needs more SNR to reach 80% under this convention. No smoothing or uncertainty interval. This result is provisional until evaluation isolation is verified.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 13
04 RESULTS
Class confusion at +4 dB
Appendix: row-normalized confusion matrices, values in percent
EE136: Machine Learning for Wireless Communications
Slide 13 of 14
Baseline
 | BP | QP | 8P | 16Q | 64Q | P4 | CF | GF
BPSK | 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0
QPSK | 0 | 73 | 23 | 4 | 0 | 0 | 0 | 0
8PSK | 0 | 8 | 85 | 8 | 0 | 0 | 0 | 0
16QAM | 0 | 0 | 0 | 10 | 90 | 0 | 0 | 0
64QAM | 0 | 0 | 5 | 33 | 62 | 0 | 0 | 0
PAM4 | 0 | 0 | 0 | 0 | 0 | 100 | 0 | 0
CPFSK | 0 | 0 | 0 | 0 | 0 | 0 | 81 | 19
GFSK | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 87
Augmented
 | BP | QP | 8P | 16Q | 64Q | P4 | CF | GF
BPSK | 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0
QPSK | 0 | 65 | 27 | 8 | 0 | 0 | 0 | 0
8PSK | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0
16QAM | 0 | 0 | 0 | 50 | 50 | 0 | 0 | 0
64QAM | 0 | 0 | 10 | 38 | 52 | 0 | 0 | 0
PAM4 | 0 | 0 | 0 | 0 | 0 | 100 | 0 | 0
CPFSK | 0 | 0 | 0 | 0 | 0 | 0 | 71 | 29
GFSK | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 87
Rows = true class Columns = predicted class Each row totals approximately 100%
Notes: Required operational point +4 dB from benchmark_results.json. Matrices use common class ordering, scale and normalization.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR

## Slide 14
04 RESULTS
Class confusion at +14 dB
Appendix: row-normalized confusion matrices, values in percent
EE136: Machine Learning for Wireless Communications
Slide 14 of 14
Baseline
 | BP | QP | 8P | 16Q | 64Q | P4 | CF | GF
BPSK | 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0
QPSK | 0 | 87 | 13 | 0 | 0 | 0 | 0 | 0
8PSK | 0 | 8 | 92 | 0 | 0 | 0 | 0 | 0
16QAM | 0 | 0 | 0 | 29 | 71 | 0 | 0 | 0
64QAM | 0 | 0 | 0 | 24 | 76 | 0 | 0 | 0
PAM4 | 0 | 0 | 0 | 0 | 0 | 100 | 0 | 0
CPFSK | 0 | 0 | 0 | 0 | 0 | 0 | 94 | 6
GFSK | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 92
Augmented
 | BP | QP | 8P | 16Q | 64Q | P4 | CF | GF
BPSK | 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0
QPSK | 0 | 53 | 47 | 0 | 0 | 0 | 0 | 0
8PSK | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0
16QAM | 0 | 0 | 0 | 53 | 47 | 0 | 0 | 0
64QAM | 0 | 0 | 0 | 47 | 53 | 0 | 0 | 0
PAM4 | 0 | 0 | 0 | 0 | 0 | 100 | 0 | 0
CPFSK | 0 | 0 | 0 | 0 | 0 | 0 | 87 | 12
GFSK | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100
Rows = true class Columns = predicted class Each row totals approximately 100%
Notes: Required operational point +14 dB from benchmark_results.json. Matrices use common class ordering, scale and normalization.
Sources: repository snapshot, slide_style_requirements.md, train.py, evaluate.py, models/network.py, models/transforms.py, checkpoint/benchmark_results.json. https://github.com/camorcam/Data_Augmentation_and_Noise_Resilience_for_Low_SNR